## Slide 1
COMPUTER NETWORKS
24Cs2202
Topic:
ERROr CORRECTION & DETECTION
Session –10

## Slide 2
AIM OF THE SESSION
To familiarize students with the basic idea of Error Control in Data link layer.
INSTRUCTIONAL OBJECTIVES
This Session is designed to:
Describe different types of errors.
Understand different types of error detection methods.
Understand error correction mechanism.
LEARNING OUTCOMES
At the end of this session, you should be able to:
Identify the types of errors.
Apply different error detection techniques to identify the error.
Apply hamming code to detect and correct the error in the data.

## Slide 3: Error Detection and Correction
Types of Errors
Error Detection
Error Correction

## Slide 4: Introduction
Data can be corrupted during transmission. For reliable communication, error must be detected and corrected.
Error Detection and Correction are implemented either at the data link layer or the transport layer of the OSI model.

## Slide 5: Type of Errors

## Slide 6: Type of Errors(cont’d)
Single-Bit Error: Only one bit in the data unit has changed
Multiple-Bit Error: Two or more nonconsecutive bits in the data unit have changed.
Burst Error: Two or more consecutive bits in the data unit have changed

## Slide 7: Type of Errors(cont’d)
Multiple-Bit Error: is when two or more nonconsecutive bits in the data unit have changed.

## Slide 8: Type of Errors(cont’d)
Burst Error means that 2 or more consecutive bits in the data unit have changed

## Slide 9: Error Detection

## Slide 10: Error Detection
Error detection uses the concept of redundancy, which means adding extra bits for detecting errors at the destination.
BLOCK CODING:
  In block coding, we divide our message into blocks, each of k bits, called datawords.
  We add r redundant bits to each block to make the length n = k + r.
  The resulting n-bit blocks are called codewords.

## Slide 11: The structure of encoder and decoder
To detect or correct errors, we need to send redundant bits

## Slide 12
Error Detection Methods

## Slide 13: Error Detection Methods
Detection methods

## Slide 14: 1. Parity Method

## Slide 15: Simple Parity Method
1. Parity Check:
  A parity bit is added to every data unit so that the total number of 1s(including the parity bit) becomes even for even-parity check or odd for odd-parity check.
  Simple parity check

## Slide 16: Parity method examples
Example 1
Suppose the sender wants to send the word “world”.
In ASCII the five characters are coded as
1110111 1101111 1110010 1101100 1100100
Sent data:
11101110
11011110
11100100
11011000
11001001

## Slide 17: Drawback of Simple Parity
M = 1100101
Parity followed: Even
Sent Message | Received Message | Parity | Message Status
11001010 | 11001110 | Odd | Discard
11001010 | 11101110 | Even | Accept
11001010 | 11101100 | Odd | Discard
11001010 | 10101100 | Even | Accept
Disadvantage: With Simple parity method, only the odd number errors can be detected.

## Slide 18: Two-Dimensional Parity Method

## Slide 19: Two-dimensional parity-check code

## Slide 20: Two-dimensional parity-check code…

## Slide 21: 2. Cyclic Redundancy Check (CRC)

## Slide 22: 2. Cyclic Redundancy Check (CRC):
Cyclic Redundancy Check (CRC) is an error detection method.
It is based on binary division.
CRC Generator-
CRC generator is an algebraic polynomial represented as a bit pattern.
Bit pattern is obtained from the CRC generator using the following rule-
Example-
Consider the CRC generator is x7 + x6 + x4 + x3 + x + 1. The corresponding binary pattern is obtained as-
The power of each term gives the position of the bit and the coefficient gives the value of the bit.

## Slide 23: Steps in Computing CRC:
Step-01: Calculation Of CRC At Sender Side-
At sender side,
A string of n 0’s is appended to the data unit to be transmitted.
Here, n is one less than the number of bits in CRC generator.
Binary division is performed of the resultant string with the CRC generator.
After division, the remainder so obtained is called as CRC.
It may be noted that CRC also consists of n bits.
Step-02: Appending CRC To Data Unit-
At sender side,
The CRC is obtained after the binary division.
The string of n 0’s appended to the data unit earlier is replaced by the CRC remainder.
Step-03: Transmission To Receiver-
The newly formed code word (Original data + CRC) is transmitted to the receiver.

## Slide 24: Steps in Computing CRC…
Step-04: Checking at Receiver Side-
At receiver side,
The transmitted code word is received.
The received code word is divided with the same CRC generator.
On division, the remainder so obtained is checked.
The following two cases are possible-
Case-01: Remainder = 0
If the remainder is zero,
Receiver assumes that no error occurred in the data during the transmission.
Receiver accepts the data.
Case-02: Remainder ≠ 0
If the remainder is non-zero,
Receiver assumes that some error occurred in the data during the transmission.
Receiver rejects the data and asks the sender for retransmission.

## Slide 25: CRC Example : Solution

## Slide 26: CRC Example : Solution

## Slide 27: 3. Checksum

## Slide 28: 3. Checksum…
Checksum is the error detection method used by upper layer protocols and is considered to be more reliable than Parity and CRC.
For error detection by checksums, data is divided into fixed sized frames or segments.
Sender’s End − The sender adds the segments using 1’s complement arithmetic to get the sum. It then complements the sum to get the checksum and sends it along with the data frames.
Receiver’s End − The receiver adds the incoming segments along with the checksum using 1’s complement arithmetic to get the sum and then complements it.
If the result is zero, the received frames are accepted; otherwise they are discarded.

## Slide 29: 3. Checksum…
Example: Suppose that the sender wants to send 4 frames each of 8 bits, where the frames are 11001100, 10101010, 11110000 and 11000011.
The sender adds the bits using 1s complement arithmetic. While adding two numbers using 1s complement arithmetic, if there is a carry over, it is added to the sum.
After adding all the 4 frames, the sender complements the sum to get the checksum, 11010011, and sends it along with the data frames.
The receiver performs 1s complement arithmetic sum of all the frames including the checksum. The result is complemented and found to be 0. Hence, the receiver assumes that no error has occurred.
11001100 | 10101010 | 11110000 | 11000011 | 11010011

## Slide 31: Practice Questions
1. The message 1101011011 is to be transmitted using the generator polynomial x4+x+1 to protect it from errors. Find the final data to be transmitted after performing CRC.
2. Original data is 10110011 10101011 01011010 11010101. Perform 2D parity and compute the codeword.
3. Original data is 10110011 10101011 01011010 11010101. Find out the checksum to detect error.

## Slide 32
SELF-ASSESSMENT QUESTIONS
What is the codeword for the dataword 1011 when even parity is used?
10110
10111
10011
10010
What is the drawback of simple parity method?
Detects only odd no. of errors
Detects only even no. of errors
Both a & b
Neither a nor b
3. Codeword means?
Dataword
Redundant bits
Dataword + Redundant bits
None

## Slide 33
SELF-ASSESSMENT QUESTIONS
What is the codeword for the dataword 1011 when even parity is used?
10110
10111
10011
10010
What is the drawback of simple parity method?
Detects only odd no. of errors
Detects only even no. of errors
Both a & b
Neither a nor b
3. Codeword means?
Dataword
Redundant bits
Dataword + Redundant bits
None

## Slide 34
Types of Errors
Error Detection Methods
Error Correction Methods
SUMMARY

## Slide 35
TERMINAL QUESTIONS
1. The message 1101011011 is to be transmitted using the generator polynomial x4+x+1 to protect it from errors. Find the final data to be transmitted after performing CRC.
2. Original data is 10110011 10101011 01011010 11010101. Perform 2D parity and compute the codeword.
3. Original data is 10110011 10101011 01011010 11010101. Find out the checksum to detect error.
4. Similarly, if Shradha is receiving a 7-bit hamming code 1011101, assume Even parity and state whether received data is correct or not. If not locate the error bit?

## Slide 36
REFERENCES FOR FURTHER LEARNING OF THE SESSION
Reference Books:
Behrouz A. Forouzan , “Data Communication and Networking”, TMH, 6th Edition ,(2012).
A.S. Tanenbaum, David J. Wetheral “Computer Networks” Pearson, 5th –Edition-(2011).
Sites and Web links:
https://www.tutorialspoint.com/data_communication_computer_network/error_detection_and_correction.htm

## Slide 37
THANK YOU
Team – COMPUTER NETWORKS